## Slide 1
LAB 02 · FIRST HANDS-ON SESSION
COAL Lab 2:
Basic Assembly
Programming
Muhammad Hashir Shaikh
Our first programs that put characters on the screen.
AH & DL
MOV
INT 21H
EMU8086
emulator screen
A
HELLO
Hashir
three programs you will write today
Notes: Lab 2. This is the first lab where students write and run real code. Keep the slides to about 20 minutes. The rest of the session is the practical. Point at the screen on the right: by the end of today they will have printed a letter, a word, and their own name.

## Slide 2
1 · THE PLAN
What are we doing today?
One idea for the whole lab: our code puts a character on the screen.
COAL · LAB 02
02
YOUR CODE
You write the instructions.
REGISTERS
The CPU holds the values.
DOS SERVICE
DOS does the printing.
SCREEN
You see the result.
mov dl, 'A'
mov ah, 2
int 21h
AH
2
DL
'A'
INT 21h
AH = 2 → print
A
By the end of today, a program you wrote will print your name.
Notes: Walk the chain left to right. We write instructions. They put values into two registers. We ask DOS to do the printing. The character shows up. Every program today is this same chain, repeated.

## Slide 3
2 · PROGRAM STRUCTURE
Anatomy of an Assembly program
The same frame every time. Your code goes in the middle.
COAL · LAB 02
03
; your code goes here
.model small
Program size. Small is plenty for us.
.stack 100h
Working memory. Just keep this line.
.data
Variables go here. Empty today.
.code
Instructions start below this line.
main proc
Our program starts here.
Today's work goes in here.
main endp
Our program ends here.
end main
End of the file. Start running at main.
Notes: Do not explain every directive in depth. They only need to know this frame is always the same. The top four lines set things up. main proc and main endp wrap our code. end main closes the file. Lab 1 used UPPERCASE. Today we write lowercase. The assembler accepts both.

## Slide 4
3 · REGISTERS
Only two registers today: AH and DL
A register is a small storage box inside the CPU.
COAL · LAB 02
04
INSIDE THE CPU
AH
2
DL
'A'
AH · THE JOB
Tells DOS which service we want.
mov ah, 2 2 means: print a character
DL · THE DATA
Holds the character we want to print.
mov dl, 'A' the character A
From Lab 1: AH is the high half of AX, and DL is the low half of DX. That is all we need today.
Notes: Keep this short. A register is a small box inside the CPU. We use two boxes today. AH holds a job number for DOS. DL holds the character. Do not go through the other registers. Lab 1 already showed the full set.

## Slide 5
4 · MOV
MOV puts a value into a register
Read it like an equals sign: the value on the right goes into the register on the left.
COAL · LAB 02
05
mov
dl,
'A'
COPY
DESTINATION
SOURCE
read it as
DL
=
'A'
like x = 5 in C++ or Python
BEFORE
AFTER
DL
?
mov dl, 'A'
DL
'A'
AH
?
mov ah, 2
AH
2
Whatever was in the register before gets replaced.
Notes: MOV copies a value into a register. Destination first, source second, like Lab 1 showed. The easiest way to read it: mov dl, 'A' means DL = 'A'. Nothing is printed yet. MOV only fills the box.

## Slide 6
5 · CHARACTER OUTPUT
Printing one character
Three lines. Fill DL, fill AH, then ask DOS to do the job.
COAL · LAB 02
06
1
mov dl, 'A'
2
mov ah, 2
3
int 21h
DL
'A'
AH
2
DOS
A
'A' goes into DL.
2 goes into AH.
2 means: print a character.
DOS checks AH, sees 2,
and prints what is in DL.
Order matters: fill DL and AH first. INT 21h uses whatever they hold at that moment.
02h and 2 are the same value. The h just means the number is written in hexadecimal.
Notes: This is the core of the lab. Three lines print one character. Line 1 puts the character in DL. Line 2 puts the job number 2 in AH. Line 3, INT 21h, hands control to DOS. DOS looks at AH to know the job, and at DL to know the character. Ask: what happens if we swap line 1 and line 2? Nothing changes. Both are ready before INT 21h.

## Slide 7
5 · CHARACTER OUTPUT
Your first complete program
COAL · LAB 02
07
.model small
.stack 100h
.data
.code
main proc
mov dl, 'A'
mov ah, 2
int 21h
mov ah, 4ch
int 21h
main endp
end main
emulator screen
A
PRINT ONE CHARACTER
Put 'A' in DL, choose service 2, call DOS.
END THE PROGRAM
Service 4Ch means: stop and go back to DOS. Every program ends with these two lines.
Notes: Type this one live in EMU8086 if you can. Emulate, then run. The amber part prints. The green part ends the program: 4Ch is the DOS service for "stop and return". Without those two lines the CPU keeps running whatever bytes come next, and the program does not end cleanly.

## Slide 8
6 · MORE CHARACTERS
Printing more than one character
Same three lines for every character. Only the character in DL changes.
COAL · LAB 02
08
mov dl, 'H'
mov ah, 2
int 21h
H
mov dl, 'E'
mov ah, 2
int 21h
E
mov dl, 'L'
mov ah, 2
int 21h
L
mov dl, 'L'
mov ah, 2
int 21h
L
mov dl, 'O'
mov ah, 2
int 21h
O
On screen:
HELLO
15 lines for 5 letters. A later lab shows a shorter way. Today, type every line.
Notes: Nothing new here. Just repetition. Point out that only the character in DL changes. Lines 2 and 3 are identical every time. If a student asks about a shorter way: yes, loops, in a later lab. Not today.

## Slide 9
7 · CHARACTERS VS NUMBERS
'5' is not the same as 5
The quotes change everything.
COAL · LAB 02
09
WITH QUOTES · A CHARACTER
mov dl, '5'
DL
53
the code for '5'
5
prints 5
NO QUOTES · A NUMBER
mov dl, 5
DL
5
just the number 5
?
prints a strange symbol
'5' with quotes is the character. 5 without quotes is a plain number.
Lab 1: characters are stored as numbers. '5' is stored as 53, and 'A' as 65.
Notes: Common mistake, so show it now. With quotes, the assembler puts the code for the character 5 into DL. That code is 53, from the ASCII ranges in Lab 1. Without quotes, DL gets the plain number 5, which is not a digit character. You get an odd symbol. Do not go into conversion or arithmetic. That comes later.

## Slide 10
8 · NEW LINE
Moving to a new line
13 and 10 are codes for invisible characters that move the cursor. No quotes.
COAL · LAB 02
10
WHERE THE CURSOR GOES
HELLO
13 back to the start
10 down one line
the next character lands here
mov dl, 13 ; carriage return
mov ah, 2
int 21h
mov dl, 10 ; line feed
mov ah, 2
int 21h
13
CARRIAGE RETURN
Cursor goes back to the start of the line.
10
LINE FEED
Cursor goes down one line.
Notes: 13 and 10 are character codes, but they do not draw anything. They move the cursor. 13, carriage return: back to the start of the current line. 10, line feed: down one line. Use both, 13 then 10, to start a fresh line. The names come from old typewriters. In Example 6 they will see what happens with only 10.

## Slide 11
9 · A FULL PROGRAM
Putting it together
Print, new line, print, end. Every program today follows this pattern.
COAL · LAB 02
11
.model small .stack 100h .data .code main proc
5 lines
H
e
l
l
o
15 lines
new line: 13, 10
6 lines
M
y
n
a
m
e
i
s
H
a
s
h
i
r
51 lines
end: 4Ch
2 lines
main endp end main
2 lines
= one character = 3 lines of code
= a space
emulator screen
Hello
My name is Hashir
A SPACE IS A CHARACTER TOO
mov dl, ' ' ; space
mov ah, 2
int 21h
About 80 lines of code for two lines of text. That is normal today. Your turn next.
Notes: This is the bridge to the practical. Nothing new, only combining. Each amber tile is one character, which means three lines of code. The teal block is the new line. The green block ends the program. Point out the space: it is a character like any other, written ' ' with a space between the quotes. The full code for programs like this is in the handout.

## Slide 12
10 · QUICK CHECK
Can you answer these?
Answer out loud. No notes, no scrolling back.
COAL · LAB 02
12
1
What goes into DL?
mov dl, ___
2
What does AH = 2 mean?
mov ah, 2
3
What does INT 21h do?
int 21h
4
How do we move to a new line?
mov dl, ?? ; twice
Notes: Answers: 1. The character we want to print, in quotes, for example 'A'. 2. It picks DOS service 2: print the character in DL. 3. It calls DOS, which does the job that AH asks for. 4. Print 13 (carriage return), then 10 (line feed), each with AH = 2 and INT 21h. Bonus if there is time: what does mov dl, 5 print? A strange symbol, not 5.

## Slide 13
PRACTICAL
COAL · LAB 02
13
Now you code.
Open EMU8086 and type every example yourself. No copy and paste: typing it is how it sticks.
IN EMU8086
1
Click new, then choose empty workspace.
2
Type the code from your handout.
3
Click emulate. Fix any errors it reports.
4
Click run. Your output appears in the emulator screen.
FOR EVERY EXAMPLE
1 Type it
2 Run it
3 Change one thing
4 Run it again
next example
Examples 1 to 6 → Final task → Submit before you leave
Notes: Hand out the practical sheet now. Insist on typing, not pasting. Typos are part of learning where the errors come from. Walk around. The most common problems: missing quotes, missing int 21h, and forgetting the 4Ch exit. The final task is in the handout. Students submit the .asm file and a screenshot of the output.