## Slide 1
LAB 03 · 8086 ASSEMBLY
COAL Lab 3:
Input & Basic
Operations
Muhammad Hashir Shaikh
Today our programs start listening to the keyboard.
INPUT
ECHO
ASCII
ADD & SUB
emulator screen
kk
ab
gh
you type one letter, the program answers
Notes: Lab 3. Last week the programs only printed. This week they read keys from the keyboard, and do very small sums. Keep the slides to about 20 minutes. Most of the two hours is the practical. On the screen: in each line, the student typed the first letter and the program printed the second.

## Slide 2
QUICK RECAP · LAB 2
What you already know
Printing one character takes three pieces. We use all of them again today.
COAL · LAB 03
02
OUTPUT → DL
mov dl, 'A'
DL holds the character.
SERVICE → AH
mov ah, 02h
AH picks the job for DOS.
EXECUTE → INT 21H
int 21h
DOS does the job.
SCREEN
A
You see the result.
Today the direction flips: the keyboard sends a character in.
02h is the same 2 you used last lab. From today we write every service number with an h.
Notes: Two minutes at most. This is only a reminder. DL holds what we print. AH picks the DOS service. INT 21h runs it. Point out 02h: it is the same 2 from Lab 2. The h just means hexadecimal. For 0 to 9 it makes no difference.

## Slide 3
1 · CHARACTER INPUT
Taking one character as input
Two lines. DOS waits for a key, then hands it to your program in AL.
COAL · LAB 03
03
1
mov ah, 01h
2
int 21h
Choose service 01h:
read one key.
DOS waits for a key.
Your program pauses here.
WHAT HAPPENS WHEN YOU PRESS K
k
you press k
INT 21h
AH = 01h
AL
'k'
the key is now in AL
KEEP A COPY
AL only holds the latest key, and printing changes AL too.
Need the key later? Copy it to another register:
mov bl, al
BL is another storage box, like DL.
AL is the low half of AX, just like DL is the low half of DX.
Notes: The two lines are the whole idea: pick service 01h, then call DOS. The program stops at INT 21h and waits until a key is pressed. That surprises students: it looks frozen, but it is waiting. The key comes back in AL. Nothing is printed by our code yet. Mention the copy now, because they will need it in Example 3: every INT 21h can change AL, so mov bl, al keeps a safe copy.

## Slide 4
2 · ECHO OR NO ECHO
Input with echo, and without
Both wait for a key and put it in AL. The only difference is what the screen shows.
COAL · LAB 03
04
AH = 01H · WITH ECHO
mov ah, 01h
int 21h
k
k
screen
AL
'k'
your program
The key appears as you type it.
AH = 07H · NO ECHO
mov ah, 07h
int 21h
k
screen
AL
'k'
your program
Nothing appears. Good for a PIN or a secret key.
01h shows the key. 07h hides it. Either way, the key lands in AL.
Notes: Same two lines, one number changes. 01h: DOS prints the key as you press it. That printing is called the echo. 07h: DOS does not print it. The key still arrives in AL. Do not go further than this. No strings, no reading a whole line. One key at a time.

## Slide 5
3 · ASCII
Every character is stored as a number
The ASCII table gives each character a code. Today we use the decimal codes.
COAL · LAB 03
05
DIGITS
'0' to '9'
→
48 to 57
0
48
1
49
2
50
9
57
…
CAPITAL LETTERS
'A' to 'Z'
→
65 to 90
A
65
B
66
C
67
Z
90
…
SMALL LETTERS
'a' to 'z'
→
97 to 122
a
97
b
98
c
99
z
122
…
ALSO USEFUL
32
space
13
carriage return
10
line feed
Each range is in order: 'B' is one more than 'A'. Remember this for ADD.
EMU8086's registers panel shows these codes in hex, so 'A' shows there as 41. Today we stay in decimal.
Notes: Lab 1 showed the ASCII table. Here we only need three ranges and three extra codes. The key point: a character is really a number. When a student presses A, AL gets 65. The ranges are in order, which is why adding 1 to a letter gives the next letter. We use that later today. Stay in decimal. Only mention hex so the registers panel does not confuse them.

## Slide 6
4 · ADD
ADD: add a number to a register
Put a number in AL, then add to it. The answer stays in AL.
COAL · LAB 03
06
mov al, 5
add al, 3
READ THE SECOND LINE AS
AL = AL + 3
AL
5
ADD 3
AL
8
before
after
The answer replaces the old value in AL.
Nothing is printed. To see AL: click emulate, then single step, and watch the registers panel.
Keep every value between 0 and 9 today. Bigger sums come in a later lab.
Notes: mov al, 5 puts the plain number 5 in AL. No quotes: this is a number, not a character. add al, 3 means AL = AL + 3. The old 5 is replaced by 8. Nothing appears on the screen. Show single step in EMU8086 and point at AL in the registers panel. Stop here. No sums of typed digits, no numbers above 9.

## Slide 7
5 · SUB
SUB: take a number away
The same idea in the other direction.
COAL · LAB 03
07
mov al, 8
sub al, 3
READ THE SECOND LINE AS
AL = AL - 3
AL
8
SUB 3
AL
5
before
after
The answer replaces the old value in AL.
Nothing is printed. To see AL: click emulate, then single step, and watch the registers panel.
Keep every value between 0 and 9 today. Bigger sums come in a later lab.
Notes: sub al, 3 means AL = AL - 3. 8 becomes 5. Again the answer replaces the old value, and again nothing is printed. Keep results at 0 or above. Going below 0 gives values that belong to a later lab.

## Slide 8
6 · CHARACTER OR NUMBER?
'5' and 5 are not the same
Quotes mean a character. No quotes means a plain number.
COAL · LAB 03
08
WITH QUOTES · A CHARACTER
mov dl, '5'
DL
53
the code for '5'
use it to print a 5
NO QUOTES · A NUMBER
mov al, 5
AL
5
just the number 5
use it with add and sub
THIS IS WHY IT MATTERS TODAY
5
you press 5
AL = 53
The keyboard always gives you a character: '5', which is 53, not the number 5.
Turning a typed digit into a number for sums comes in a later lab.
Notes: With quotes, the assembler stores the ASCII code of the character. '5' becomes 53. Without quotes, it is the plain number 5. That is what add and sub work with today. The link to input: when a student types 5, AL gets 53. If they add 3 to that, they get 56, which prints as 8. It looks right by luck, so warn them now. Do not teach conversion. Just make them aware of it.

## Slide 9
7 · PUTTING IT TOGETHER
Read a key, print the next one
Input, ASCII and ADD in six lines.
COAL · LAB 03
09
mov ah, 01h ; read a key, with echo
int 21h ; AL = the key
mov dl, al ; copy it into DL
add dl, 1 ; one more: the next character
mov ah, 02h ; print a character
int 21h ; show it
c
you press c
AL
99
'c' is 99
DL
100
copied from AL, then + 1
cd
c is the echo, d is printed: 100 is d
In Example 6 there is a new line in the middle. Printing changes AL, so save the key first with mov bl, al.
Notes: Nothing new, only combining. Read a key: it lands in AL. Copy it to DL. Add 1. Print DL. Because c is 99 in the ASCII table, adding 1 gives 100, and 100 is d. Ask: what do you get if you press 4? (5, digits are in order too.) What if you press z? (123, which is {, not a letter.)

## Slide 10
8 · QUICK CHECK
Can you answer these?
Answer out loud. No notes, no scrolling back.
COAL · LAB 03
10
1
Which register gets the key you press?
mov ah, 01h
2
What is the difference between 01h and 07h?
mov ah, 07h
3
What is the ASCII range for capital letters?
'A' to 'Z'
4
What does this line do?
add al, 3
Notes: Answers: 1. AL. The key arrives in AL after INT 21h. 2. Both read one key into AL. 01h shows it on the screen (echo). 07h does not. 3. 65 to 90. Small letters are 97 to 122, digits 48 to 57. 4. AL = AL + 3. The answer stays in AL. Bonus if there is time: the user types 5. What number is in AL? (53.)

## Slide 11
PRACTICAL
COAL · LAB 03
11
Now you code.
Open EMU8086 and type every example yourself. No copy and paste: typing it is how it sticks.
TODAY IN EMU8086
1
A program that reads a key waits. Click the emulator screen, then press a key.
2
Examples 4 and 5 print nothing: single step, watch AL.
3
The registers panel shows hex. 'A' shows as 41 there.
4
Printing changes AL. Save a key with mov bl, al.
FOR EVERY EXAMPLE
1 Type it
2 Run it
3 Change one thing
4 Run it again
next example
Examples 1 to 6 → Practice tasks → Final task → Submit
Notes: Hand out the practical sheet now. Insist on typing, not pasting. Walk around. The most common problems today: the program looks frozen (it is waiting for a key), the key is lost after a new line (not saved in BL), and confusion about hex in the registers panel. Practice tasks are not submitted. The final task is: students submit the .asm file and two screenshots.