## Slide 1
LAB 04 · 8086 ASSEMBLY
COAL Lab 4:
Loops in 8086
Assembly
Muhammad Hashir Shaikh
Today one block of code runs again and again.
CX
LABELS
LOOP
INC & DEC
emulator screen
*****
12345
write it once, the loop repeats it
Notes: Lab 4. Until now every line ran once. Today a block of lines runs as many times as we ask. Keep the slides to about 15 minutes. Most of the lab is the practical. On the screen: both lines come from one short loop each. By the end of the slides they will write both.

## Slide 2
LAB 04 · 8086 ASSEMBLY
AX: Accumulator Register (used in arithmetic, logic, and I/O operations)
BX: Base Register (used as a memory pointer or offset storage)
CX: Counter Register (used as a loop counter and in shift/rotate instructions)
DX: Data Register (used in I/O port addressing, multiplication, and division)
Notes: Lab 4. Until now every line ran once. Today a block of lines runs as many times as we ask. Keep the slides to about 15 minutes. Most of the lab is the practical. On the screen: both lines come from one short loop each. By the end of the slides they will write both.

## Slide 3
1 · WHY LOOPS
Five stars, two ways
Same output. Look at how much code each one needs.
COAL · LAB 04
02
WITHOUT A LOOP · 15 LINES
mov dl, '*' ; star 1
mov ah, 02h
int 21h
mov dl, '*' ; star 2
mov ah, 02h
int 21h
mov dl, '*' ; star 3
mov ah, 02h
int 21h
mov dl, '*' ; star 4
mov ah, 02h
int 21h
mov dl, '*' ; star 5
mov ah, 02h
int 21h
WITH A LOOP · WRITE IT ONCE
mov dl, '*'
mov ah, 02h
int 21h
repeat
5 times
*****
same output
3 lines, written once.
100 stars? Without a loop: 300 lines. With a loop: change one number.
Notes: Ask first: how would you print five stars with what you know? They will copy the three lines five times. That works, but it does not scale. 100 stars would be 300 lines. A loop lets us write the three lines once and say how many times to run them. The next slides show how.

## Slide 4
2 · THE COUNTER
CX counts the turns
Put the number of turns in CX before the loop. Each turn takes 1 away.
COAL · LAB 04
03
mov cx, 5
CX
5
The counter register.
LOOP checks it every turn.
WHAT HAPPENS TO CX
5
turn 1
−1
4
turn 2
−1
3
turn 3
−1
2
turn 4
−1
1
turn 5
−1
0
stop
5 turns, then CX is 0 and the loop ends.
CL is the low half of CX, just like AL is the low half of AX. Leave CL alone while a loop runs.
Notes: CX is the count register. The LOOP instruction always uses CX, no other register. We set CX once, before the loop. Every turn, LOOP takes 1 away. When CX reaches 0 the loop stops. Starting at 5 gives 5 turns: 5, 4, 3, 2, 1. At 0 it stops. Warn them now: CL is part of CX. If they use CL to store a key inside a loop, they break the count.

## Slide 5
3 · LABELS
A label marks where to go back to
Give a line a name. LOOP jumps back to that name.
COAL · LAB 04
04
again:
; instructions
; to repeat
loop again
jump
back
THE SPOT TO COME BACK TO
again:
colon at the end
THE JUMP BACK
loop again
no colon here
ANY NAME WORKS
again print L1 same name in both places
A label does nothing by itself. It is a bookmark for a line.
Notes: A label is just a name for a line. It is not an instruction and the CPU does nothing when it reaches it. Where we write it with a colon, again:, we mark the spot. loop again (no colon) says: go back to that spot. The name is our choice. It only has to match in both places.

## Slide 6
4 · LOOP
LOOP: repeat a block CX times
Set CX, mark the start with a label, end the block with loop.
COAL · LAB 04
05
mov cx, 5 ; 5 turns
again:
mov dl, '*' ; the star
mov ah, 02h ; print DL
int 21h
loop again ; CX - 1, go back
OUTPUT
*****
WHAT loop again DOES
1
CX = CX − 1
2
CX not 0? Jump back to again.
3
CX is 0? Go on to the next line.
CX = 5
print *
CX − 1
CX = 0 ?
stop
yes
no: go back and repeat
Notes: This is the whole pattern. Three parts: set CX, the label, the loop line. The body between the label and loop is the three print lines they already know. loop again does two things: takes 1 from CX, then jumps back if CX is not 0. Service 02h with an h, as in Lab 3.

## Slide 7
5 · TRACING
Follow CX one turn at a time
Read top to bottom. This is what single step shows you.
COAL · LAB 04
06
TURN
CX
PRINTS
AFTER loop again
SCREEN
1
5
*
CX = 4 back to again
*
2
4
*
CX = 3 back to again
**
3
3
*
CX = 2 back to again
***
4
2
*
CX = 1 back to again
****
5
1
*
CX = 0 stop, go to the next line
*****
5 turns, 5 stars. loop takes 1 from CX first, then checks for 0.
In EMU8086, click single step and watch CX in the registers panel: 0005, 0004, 0003, 0002, 0001, 0000.
Notes: Go row by row with the class. Ask them to say the next row before you reveal it. The CX column is CX when the turn starts. The last column is CX after loop has taken 1 away. The key moment is row 5: CX becomes 0, so loop does not jump back. If there is time, show it live with single step.

## Slide 8
6 · INC AND DEC
INC and DEC: one up, one down
Short ways to add 1 or take 1 away.
COAL · LAB 04
07
INC · ONE UP
mov dl, '1'
inc dl
DL
'1'
inc
DL
'2'
code 49
code 50
inc dl is the same as add dl, 1
DEC · ONE DOWN
mov dl, '5'
dec dl
DL
'5'
dec
DL
'4'
code 53
code 52
dec dl is the same as sub dl, 1
inc adds 1 to the ASCII code, so 'A' becomes 'B' and '1' becomes '2'.
Notes: Two small instructions. inc adds 1, dec takes 1 away. Nothing else. They already know add dl, 1 from Lab 3. inc dl does the same thing in a shorter way. Link to ASCII: '1' is 49, add 1 and it is 50, which is '2'. Digits and letters are in order. Do not go further. We only need inc for the next slide.

## Slide 9
7 · PUTTING IT TOGETHER
Print 12345 with one loop
LOOP repeats the block. INC changes the character each turn.
COAL · LAB 04
08
mov cx, 5 ; 5 turns
mov dl, '1' ; start at '1'
again:
mov ah, 02h ; print DL
int 21h
inc dl ; next digit
loop again ; CX - 1, go back
DL ON EACH TURN
'1'
49
CX 5
'2'
50
CX 4
'3'
51
CX 3
'4'
52
CX 2
'5'
53
CX 1
12345
one loop, five different characters
Keep mov dl, '1' above the label. Inside the loop it would reset DL every turn, and you would get 11111.
Notes: Nothing new here, only combining LOOP, INC and ASCII. DL starts at '1'. Each turn prints DL, then inc moves it to the next digit. Printing with 02h does not change DL, so the value carries into the next turn. Ask: what if mov dl, '1' moves below again:? (11111.) What if we start at 'A'? (ABCDE.) What if CX is 9? (123456789.)

## Slide 10
PRACTICAL
COAL · LAB 04
09
Now you code.
Open EMU8086 and type every example yourself. No copy and paste: typing it is how it sticks.
TODAY IN EMU8086
1
Set CX before the label. Set it inside and the loop never ends.
2
Click single step and watch CX drop by 1 each turn.
3
Registers show hex: mov cx, 10 shows CX as 000A.
4
Do not store a key in CL inside a loop. CL is part of CX.
FOR EVERY EXAMPLE
1 Type it
2 Run it
3 Change one thing
4 Run it again
next example
Examples → Practice tasks → Final task → Submit
Notes: Hand out the practical sheet now. Insist on typing, not pasting. Most common problems today: mov cx placed inside the loop (it never ends), a label name that does not match, a missing colon after the label, and CL used for storage inside a loop. Show single step once on the projector so they can watch CX count down.