## Slide 1
FIRST LECTURE · NO PRIOR ASSEMBLY ASSUMED
Computer Organization
& Assembly Language
Lecture 01
Muhammad Hashir Shaikh
INTEL 8086
x86 FAMILY
REGISTERS
EMU8086
M
O
V
three letters, exactly as the machine stores them
Notes: Welcome. Set the tone: this is the course where the computer stops being a black box. No prior assembly needed. 2.5 hours today, and by the end you will recognise everything on these slides — you are not expected to write programs yet.

## Slide 2
ROADMAP
Where today takes us
Nine ideas, in order. Each one is what makes the next one possible.
01
Computers
How a machine is organised
02
CPU
The part that runs instructions
03
Architecture
Bits, x86, x64 — the vocabulary
04
8086
The processor we study
05
Registers
The CPU's own storage
06
Assembly
The language itself
07
Syntax
How it is written down
08
ASCII
Characters as numbers
09
EMU8086
Where we will run it
Today is about understanding. Writing real programs starts next lecture.
COAL · LECTURE 01
02
Notes: Walk the nine steps quickly. Emphasise the order is deliberate: you cannot understand a register until you know what a CPU is, and you cannot read assembly until you know what a register is.

## Slide 3
1 · COURSE INTRODUCTION
Welcome to COAL
You already know how to tell a computer what to do.
In Python, Java, C++ or JavaScript you write a statement and something happens. You trust it. You rarely ask what “something” actually is.
This course is about the layer underneath.
What your code turns into. What the processor really receives. Which parts of the machine do the work, and in what order.
By the end of the semester you will write programs in the processor’s own language — and the black box will be gone.
THE GAP THIS COURSE FILLS
Your program
print(x) · int main() · System.out
everything in between
← THIS COURSE
The hardware
CPU · registers · memory · buses
COAL · LECTURE 01
03
Notes: Ask the room: when you write x = a + b in C++, what actually happens? Collect a few answers. Do not correct them — just note that by lecture 3 they will be able to answer precisely.

## Slide 4
1 · COURSE INTRODUCTION
What you will learn this semester
01
Computer organization
CPU, memory, buses, input and output — and how they fit together to run a program.
02
The instruction cycle
How a processor works through a program, one instruction at a time.
03
8086 architecture
The registers, the memory model, and the parts of the chip you can actually reach.
04
Assembly language
Its syntax, its instructions, how it stores data and how it makes decisions.
05
Real programs
Written by you, assembled by you, and run in front of you — step by step.
06
The toolchain
EMU8086: editor, assembler, emulator and debugger in a single window.
Every one of these is introduced today — just at a level you can hold in your head.
COAL · LECTURE 01
04
Notes: Keep this brisk. The point is to show the shape of the semester so the detail later has somewhere to land.

## Slide 5
1 · COURSE INTRODUCTION
Why this course matters
1
It removes the magic.
You stop guessing what your code becomes. You know — because you can read it.
2
It makes you better at high-level languages.
Data sizes, memory use, and why one loop is slower than another all stop being mysterious.
3
It is the foundation of the rest of your degree.
Operating systems, compilers, embedded systems, security and reverse engineering all assume it.
4
It teaches a different way of thinking.
Precise, literal, and aware of the machine — a skill that outlives any one language.
WHAT TO EXPECT
Cumulative
Every lecture leans on the one before it. Missing one is expensive.
Hands-on
You will run your own code in EMU8086, not just read about it.
Literal
The machine does exactly what you wrote — never what you meant.
Beginner-safe
We assume you have never seen assembly. Questions are the point.
COAL · LECTURE 01
05
Notes: Reason 3 is the one that lands with students: name the later courses in your programme that depend on this one.

## Slide 6
2 · WHAT IS COAL?
The course name is two subjects joined together
COMPUTER ORGANIZATION
How the machine is built
How the major components of a computer work together to run a program — what each part is for, and how they are wired to one another.
CPU
MEMORY
REGISTERS
INPUT / OUTPUT
BUSES
ASSEMBLY LANGUAGE
How we speak to it
A low-level programming language whose statements sit very close to the instructions the processor actually carries out.
INSTRUCTIONS
REGISTERS
MEMORY
DIRECT CONTROL
One of them is the machine. The other is how we talk to it. Learning either one alone leaves you with half a picture.
COAL · LECTURE 01
06
Notes: Say the sentence at the bottom out loud twice — it is the thesis of the whole course.

## Slide 7
2 · WHAT IS COAL? — PART ONE
Computer Organization: the five words
1
CPU
The part that actually carries out instructions. The “doer”.
2
Memory
Holds the program and its data while the program is running.
3
Registers
A handful of tiny, extremely fast storage slots inside the CPU.
4
Input / Output
How the machine reads from, and writes to, the outside world.
5
Buses
The wires that carry data and addresses between all of the above.
We will draw all five of them on one diagram in a few slides — and then keep coming back to that diagram all semester.
COAL · LECTURE 01
07
Notes: Do not define these deeply yet — this is a vocabulary preview. Each gets its own treatment shortly.

## Slide 8
2 · WHAT IS COAL? — PART TWO
Assembly Language
DEFINITION
A low-level programming language in which each statement corresponds very closely to a single instruction the processor can execute.
1
Closer to the machine
Far below anything you have written before — there is almost nothing between your statement and the hardware.
2
Direct interaction with the processor
You name the processor’s own registers and memory locations yourself.
3
Nothing is hidden, nothing is decided for you
There is no compiler quietly making choices on your behalf. That is the power, and the cost.
WHAT IT LOOKS LIKE
; my first look at assembly
start:
MOV AX, BX
MOV CX, AX
Do not try to read this yet.
Today we only care what assembly looks like. What these lines actually do comes next lecture.
COAL · LECTURE 01
08
Notes: Show the code but resist every temptation to explain MOV. Students will ask — tell them they will know by the end of lecture 2, and that today the goal is fluency in reading shape, not meaning.

## Slide 9
2 · WHAT IS COAL?
Why are these two taught together?
COMPUTER ORGANIZATION
gives you the nouns
CPU · register · memory · bus
ASSEMBLY LANGUAGE
gives you the verbs
move · compare · jump · store
each one
explains the other
You cannot read an instruction without knowing the machine.
The line MOV AX, BX means nothing until you know what AX is — and AX only means something once you know what a register is.
And the machine stays abstract until you use it.
Registers, memory and buses are just boxes on a diagram until you write an instruction that actually moves a value through them.
So we learn the machine and the language side by side — each one makes the other concrete.
COAL · LECTURE 01
09
Notes: This is the answer to 'why is the course called two things'. Give a concrete example: reading disassembled output of their own C++ program is the payoff.

## Slide 10
3 · LEVELS OF PROGRAMMING LANGUAGES
Three levels, one machine
LEVEL 3 · HIGH-LEVEL LANGUAGES
Python · Java · C++ · JavaScript
Written for humans. One statement can do a great deal of work.
LEVEL 2 · ASSEMBLY LANGUAGE
MOV AX, BX
Short symbolic names instead of numbers. Roughly one statement per machine instruction.
LEVEL 1 · MACHINE LANGUAGE
10001001 11011000
Pure binary. The only thing the processor decodes and executes directly.
GOING UP
More abstraction. More convenience. The same source code runs on very different machines.
GOING DOWN
Fewer conveniences. Far more direct control over what the hardware actually does.
Assembly sits in the middle — and that is exactly why it is worth learning.
Human-friendly
Assembly
Machine-level
COAL · LECTURE 01
10
Notes: Do not get drawn into compilers and assemblers yet. If asked, say: a translator turns each level into the one below it, and we cover that properly later.

## Slide 11
3 · LEVELS OF PROGRAMMING LANGUAGES
Abstraction versus control
HIGH-LEVEL LANGUAGE
ASSEMBLY LANGUAGE
can do a great deal — a loop, a call, a whole expression
ONE STATEMENT
is roughly one machine instruction
the same source runs on many different processors
PORTABILITY
is tied to one processor family
the compiler quietly decides for you
REGISTERS & MEMORY
you decide, every single time
fast; the details are handled for you
WRITING IT
slow; every detail is yours to get right
the intent of the program
WHAT YOU SEE
exactly what the machine will do
Neither one is “better”. They sit at different distances from the hardware — and this course lives at the bottom.
COAL · LECTURE 01
11
Notes: Good place for a question: which column would you rather write a game in? Which would you rather write a device driver in? Both answers are defensible.

## Slide 12
4 · BASIC COMPUTER ORGANIZATION
The whole machine, on one diagram
Input goes in, the CPU works with memory, results come out. Everything else this semester is detail inside this picture.
INPUT
keyboard · mouse
files
CPU
THE PART THAT ACTS
Control Unit
ALU
Registers
Main Memory
RAM · BY ADDRESS
0100
0102
0104
0106
OUTPUT
screen · printer
files
STORAGE — LONG TERM
Hard disk or SSD. Keeps files when the power is off. A program is copied from storage into memory before it can run — the CPU never executes directly from here.
THE THREE BUSES — THE WIRES IN BETWEEN
ADDRESS
which location are we talking about?
DATA
the actual bytes travelling to or from it
CONTROL
is this a read, or a write?
COAL · LECTURE 01
12
Notes: Draw this on the board too. Students should be able to redraw it from memory by the end of the course. Stress: the arrows are buses, and the CPU only ever works with what is in memory or in its own registers.

## Slide 13
4 · BASIC COMPUTER ORGANIZATION
Inside the CPU: three parts
Nearly every assembly instruction you will ever write is about these three — plus memory.
CENTRAL PROCESSING UNIT
CU
Control Unit
Decides what happens next. It fetches each instruction, works out what it is, and directs the other parts. It does no arithmetic itself.
ALU
Arithmetic Logic Unit
The part that actually performs the work — calculations on numbers, and comparisons between them.
REG
Registers
A small, fixed set of storage slots inside the CPU. The fastest storage in the machine, and the ones you name in code.
Keep these names. From the moment we start writing code, “put this value in a register” and “let the ALU work it out” stop being abstractions.
COAL · LECTURE 01
13
Notes: Analogy if needed: the control unit is the foreman, the ALU is the worker, the registers are the workbench. Use it once, then drop it.

## Slide 14
4 · BASIC COMPUTER ORGANIZATION
Memory is not storage
Two words students mix up constantly. They are different things, doing different jobs.
SMALLER AND FASTER AT THE TOP
Registers
a handful of slots · instant · inside the CPU
Main memory (RAM)
billions of slots · very fast · empties when the power goes
Storage (disk / SSD)
vast · far slower · keeps its contents forever
Faster storage is always smaller and more expensive. That trade-off never goes away.
Main memory — RAM
—
Holds the running program and its data.
—
Every location has a numeric address.
—
Loses everything when the power goes off.
Storage — disk or SSD
—
Keeps files whether the machine is on or not.
—
Far larger, and far slower, than memory.
—
Code must reach memory before it can run.
COAL · LECTURE 01
14
Notes: Quick check: if you unplug the machine mid-program, what survives? Answer: only what is in storage. Everything in registers and RAM is gone.

## Slide 15
5 · HOW THE CPU WORKS
Fetch → Decode → Execute
This is the entire job of a processor. One loop, repeated until the machine is switched off.
01
FETCH
Get the next instruction.
The CPU knows the address of the next instruction. It asks memory for what is stored there, and the bytes come back.
02
DECODE
Work out what it is.
The control unit examines those bytes: which instruction is this, and what does it need to work with?
03
EXECUTE
Do it.
The instruction is carried out — the ALU, the registers or memory each do whatever that instruction asked for.
and again · billions of times a second
A processor does not “run your program”. It fetches one instruction, understands it, performs it, and goes back for the next one. Your program is just a very long list of those.
COAL · LECTURE 01
15
Notes: This is the single most important idea in the first half of the course. Say it three different ways. No pipelines, no caches, no branch prediction — if asked, say those are refinements of this same loop.

## Slide 16
5 · HOW THE CPU WORKS
The same three steps, slowly
1
Fetch
A register called IP — the instruction pointer — holds the address of the next instruction. The CPU sends that address to memory; memory sends the instruction back.
IP --> MEMORY --> instruction bytes
2
Decode
Those bytes are just numbers. The control unit takes them apart: which instruction is this, and which registers or memory locations does it involve?
bytes --> CONTROL UNIT --> which one?
3
Execute
The right part of the CPU is told to act — the ALU, a register, or memory. Afterwards IP moves along, ready for the next fetch.
CONTROL UNIT --> ALU / REGISTERS / MEMORY
Remember the name IP. It is one of the 8086’s registers, and we will meet it again in about fifteen minutes.
COAL · LECTURE 01
16
Notes: Keep it conceptual. If someone asks how the bytes encode the instruction, say: that is instruction encoding, and we cover it later in the course.

## Slide 17
6 · ARCHITECTURE TERMINOLOGY
What does “16-bit” or “64-bit” actually mean?
Processors get described by a number: 8-bit, 16-bit, 32-bit, 64-bit. It sounds like a rating. It is not.
That number is the size of the chunks of data the processor is built to handle in one go — most visibly, the width of its registers and of the values it naturally moves around.
A wider processor holds a bigger number in a single register, and can generally refer to far more memory.
HOLD ON TO THIS
“16-bit” describes how the processor is designed. It is not a speed rating, and it is not a brand name.
ONE 8-BIT REGISTER
8 bits = 1 byte · holds a value from 0 to 255
ONE 16-BIT REGISTER — LIKE THE 8086’S
16 bits = 2 bytes · holds a value from 0 to 65,535
Each little square is one bit — a single 0 or 1. The whole strip is one register. Doubling the width doubles how many bits travel together.
COAL · LECTURE 01
17
Notes: Count the squares with them for the 8-bit strip. It makes 'width' physical rather than a word.

## Slide 18
6 · ARCHITECTURE TERMINOLOGY
8 → 16 → 32 → 64
WIDTH OF ONE REGISTER
LARGEST VALUE
8-bit
1 byte
255
16-bit
2 bytes
65,535
← the 8086 lives here
32-bit
4 bytes
4,294,967,295
64-bit
8 bytes
18,446,744,073,709,551,615
Careful: wider does not mean “twice as fast”.
A wider processor handles bigger values in one step and can address far more memory. Real-world speed depends on clock rate, chip design, memory, and a dozen other things. 64-bit is a design decision, not a performance claim.
COAL · LECTURE 01
18
Notes: If a student asks why 64-bit machines felt faster: mention more memory addressable and more registers, but keep it short — this is not the lecture for it.

## Slide 19
6 · ARCHITECTURE TERMINOLOGY
x86 and x64 — clearing up the names
One of these terms is used two different ways. Knowing which is which saves a great deal of confusion.
x86
THE PROCESSOR FAMILY
Historically, the Intel family that began with the 8086 and continued with the 80186, 80286, 80386 and 80486.
Every name ends in “86” — so the family became “x86”.
x86
IN EVERYDAY SOFTWARE
In downloads, installers and folder names, “x86” is now commonly used to mean the 32-bit version of a program or system.
That is why a 64-bit Windows machine still has a folder called “Program Files (x86)”.
x64
ALSO WRITTEN X86-64
The 64-bit extension of the same x86 architecture — the same family, extended to work with 64-bit registers and far more memory.
“x64” and “x86-64” mean the same thing.
So “x86” can mean a whole processor family, or a 32-bit build of some software — read it from the context.
“x64” has only one meaning: the 64-bit extension. Our 8086 is 16-bit, and it is where the whole family started.
COAL · LECTURE 01
19
Notes: Have them open a file browser later and look for Program Files (x86). Concrete beats abstract here.

## Slide 20
7 · WHAT IS THE 8086?
The Intel 8086
intel
8086
16-BIT MICROPROCESSOR
1978
16-BIT
THE FIRST x86
INTRODUCED
1978, by Intel.
WHAT IT IS
A 16-bit microprocessor — its registers are 16 bits wide.
WHY IT MATTERS
It is the first member of what became the x86 family, the architecture that still runs most desktops and laptops.
WHAT SURVIVED
Its register names and the style of its instructions are still recognisable in today’s x86 processors.
A word of care with words
8086 is the name of a processor. “16-bit” describes its architecture — the width of its registers and the data it naturally handles. The two are not interchangeable.
WHY WE LEARN THIS ONE
Small enough to learn completely, important enough to be worth learning, and superbly supported by teaching tools such as EMU8086.
COAL · LECTURE 01
20
Notes: Do not wander into 8086 history — one sentence on 1978 is enough. The point students need is: this is the ancestor, and it is simple enough to understand in full.

## Slide 21
7 · WHAT IS THE 8086?
From one chip to every chip
1978
Intel 8086
The 16-bit processor this whole course is built around.
1982 – 1989
80286 · 80386 · 80486
The family grows. The 80386 brings 32-bit registers to the same architecture.
2000s
x86-64 / x64
A 64-bit extension is added. Still the same family, still running the old instructions.
Today
The laptop in front of you
Vastly faster and vastly more complex — and still a descendant of the 8086.
8086
x86 family
modern x86 / x64
COAL · LECTURE 01
21
Notes: The punchline: the instructions they will write in EMU8086 are, in a real sense, still understood by the machine on their desk.

## Slide 22
8 · BASIC 8086 ARCHITECTURE
Inside the 8086 — just the parts that matter today
INTEL 8086
Control Unit
fetches and decodes;
directs everything else
ALU
performs calculations
and comparisons
INTERNAL BUS
REGISTERS — THE CPU’S OWN STORAGE
AX
BX
CX
DX
SP
BP
SI
DI
ADDRESS BUS
DATA BUS
CONTROL BUS
MEMORY
Instructions and data
live out here.
0100
0102
0104
0106
0108
010A
Assembly instructions spend nearly all of their time moving values between those registers and that memory. Which is exactly why registers come next.
COAL · LECTURE 01
22
Notes: Resist going into the bus interface unit / execution unit split, segmentation, or the prefetch queue. Point at the three buses, name them, move on.

## Slide 23
9 · 8086 REGISTERS
First: what is a register?
A register is a very small, very fast storage location built directly into the CPU.
There are only a handful of them, and you cannot make more. The set is fixed by the processor’s design.
Each one has a name that you write literally in your code — AX, BX, CX, and so on.
On the 8086 the main registers hold 16 bits each: two bytes.
The CPU can use a register’s contents immediately. Fetching the same value from memory takes very much longer.
Memory is the filing cabinet across the room. Registers are the two or three sheets already lying on your desk — far fewer, but instantly to hand.
ONE 8086 REGISTER, DRAWN OUT
AX
16 bits · 2 bytes
bit 15
bit 0
Sixteen little switches, each a 0 or a 1. That is the whole register.
INSIDE THE CPU
AX
BX
CX
DX
MEMORY
far away
far slower
Registers are where an assembly program actually lives and works.
COAL · LECTURE 01
23
Notes: The desk/cabinet analogy is the only analogy worth using here. Use it once. Then insist on the real vocabulary.

## Slide 24
9 · 8086 REGISTERS
The 8086 register set
Fourteen names, in five groups. Today you need only to recognise them and know which group each belongs to.
GENERAL PURPOSE
The everyday working registers — the ones you will name most often.
AX
BX
CX
DX
POINTER & INDEX
Hold positions and addresses rather than ordinary values.
SP
BP
SI
DI
INSTRUCTION POINTER
Which instruction comes next.
IP
FLAGS
Records what just happened.
FLAGS
SEGMENT REGISTERS
Mark where code, data and the stack sit in memory.
CS
DS
SS
ES
You will have used every one of these before the semester is over. Today: recognition only.
COAL · LECTURE 01
24
Notes: Read the fourteen names out loud together. It sounds silly and it works — the names need to stop being strange before lecture 2.

## Slide 25
9 · 8086 REGISTERS
AX, BX, CX, DX — and their two halves
AX · one 16-bit register
AH
the high half · 8 bits
AL
the low half · 8 bits
bit 15
bit 8
bit 7
bit 0
AX
AH
AL
BX
BH
BL
CX
CH
CL
DX
DH
DL
H AND L
H is the high half — the upper 8 bits. L is the low half — the lower 8 bits.
TWO WAYS TO NAME IT
AX is one 16-bit register, or two 8-bit registers, depending on which name you write.
ONLY THESE FOUR
AX, BX, CX and DX split this way. SP, BP, SI and DI do not — they are 16-bit only.
COAL · LECTURE 01
25
Notes: Common exam question: what is the relationship between AX, AH and AL? Answer: AH and AL are the two halves of the same 16 bits, not separate storage.

## Slide 26
9 · 8086 REGISTERS
The other four groups
Names and jobs only. We will not use a single one of them today.
POINTER & INDEX
SP
BP
SI
DI
These hold positions and addresses rather than ordinary values: where we are in the stack, and where we are inside a block of data.
INSTRUCTION POINTER
IP
Holds the address of the next instruction to fetch — the CPU’s own “you are here” marker. This is the register from the fetch step earlier.
FLAGS
FLAGS
Single-bit indicators the CPU sets automatically to record facts about what just happened — such as whether a result came out as zero.
SEGMENT REGISTERS
CS
DS
SS
ES
Mark out where the code, the data and the stack live in memory. The 8086 uses them to reach its full memory space.
Recognition today. Usage later — each of these groups gets a lecture of its own.
COAL · LECTURE 01
26
Notes: Call back to the fetch–decode–execute slide when you reach IP. That link is what makes registers feel real rather than arbitrary.

## Slide 27
10 · ASSEMBLY LANGUAGE BASICS
The anatomy of an assembly statement
Important — we are not learning what MOV does today. That is next lecture. Right now we care only about the shape of a statement.
MOV AX, BX
mnemonic destination , source
MOV
MNEMONIC · THE INSTRUCTION
A short, readable name standing for one machine instruction. It is the verb of the statement — the thing being done.
AX
FIRST OPERAND · DESTINATION
The operand written first. In a two-operand statement of this form it is the destination — the place the instruction acts upon.
BX
SECOND OPERAND · SOURCE
The operand written second. It is the source — the place the instruction takes its value from.
COAL · LECTURE 01
27
Notes: If someone blurts out that MOV copies a value: acknowledge it, say they are ahead of the class, and move on without confirming details. Hold the line — the payoff next lecture is better.

## Slide 28
11 · ASSEMBLY SYNTAX RULES
The syntax rules that actually matter
Is assembly case-sensitive?
In EMU8086, no. Instruction names and register names are case-insensitive: MOV, mov and Mov are the same instruction, and AX, ax and Ax are the same register.
Convention: write instructions and registers in uppercase. It reads better.
Does indentation matter?
No. Unlike Python, indentation has no meaning whatsoever — the assembler ignores it completely. It exists purely so that a human can read your code.
Convention: labels at the left margin, instructions indented beneath them.
How are instructions and operands separated?
The mnemonic comes first, then its operands. Where there are two operands, a comma separates them — destination first, source second.
One instruction per line. Spaces around the comma are optional.
What am I allowed to call things?
Names you invent — labels above all — begin with a letter or an underscore, contain no spaces, and must not be a reserved word such as a register or instruction name.
AX is taken. start, myLoop and total are all fine.
Case and spacing are for humans. Commas, colons and semicolons are for the assembler.
COAL · LECTURE 01
28
Notes: The Python comparison is worth dwelling on — students carry the indentation habit in and are surprised it means nothing here.

## Slide 29
11 · ASSEMBLY SYNTAX RULES
Reading the punctuation
; -----------------------------------
; a comment starts with a semicolon
; -----------------------------------
start: ; a label names a place
MOV AX, BX ; mnemonic + 2 operands
mov cx, ax ; lowercase is fine too
NAMING RULES FOR LABELS
Letters, digits and underscores — and it must not start with a digit.
No spaces anywhere inside the name.
It must not be a register name or an instruction name — those are taken.
Write a colon after it where you define it; no colon where you refer to it.
;
Semicolon — a comment
Everything after it on that line is ignored by the assembler. Written for humans only. Use them generously.
start:
A label
A name you give to a place in your code. It ends with a colon where it is defined.
· ·
Indentation
Purely visual. It costs nothing and makes labels stand out from the instructions beneath them.
mov
Lowercase
Exactly the same instruction as MOV. EMU8086 does not distinguish between them.
COAL · LECTURE 01
29
Notes: Read the code block aloud line by line, naming punctuation only — semicolon, colon, comma. Do not say what the instructions do.

## Slide 30
12 · ANATOMY OF AN ASSEMBLY PROGRAM
The shape of a complete program
Do not memorise this. Recognise the parts — the template will be given to you.
; ================================
; Lecture 1 - program skeleton
; ================================
.MODEL SMALL ; memory model
.STACK 100H ; room for the stack
.DATA
; values are declared here
.CODE
MAIN PROC
; your instructions go here
MAIN ENDP
END MAIN
Comments
Notes for humans. The assembler ignores them entirely, and good programs are full of them.
Directives
.MODEL and .STACK are not instructions. They are messages to the assembler about how to build the program.
Data section
.DATA is where the values your program needs are declared before it runs.
Code section
.CODE is where the instructions live. MAIN PROC … MAIN ENDP wraps them into a named procedure.
The end marker
END MAIN tells the assembler that the program is complete and where it begins.
EMU8086 also offers a shorter skeleton that begins with ORG 100H. Use whichever one your lab sheet specifies — the parts are the same.
COAL · LECTURE 01
30
Notes: Point at each coloured region as you name it. Students only need to be able to say 'that part is data, that part is code' by the end.

## Slide 31
13 · INTRODUCTION TO ASCII
Characters are numbers too
A computer stores numbers. Only numbers.
There is no such thing as a letter inside memory. There are only values — and an agreement about what those values mean.
ASCII is that agreement.
It is a standard table that says which number stands for which character. When something stores the letter A, what is actually there is the number 65.
Why this matters to us: at this level, a character and its number are the same thing. You will see both spellings of one value constantly.
Standard ASCII covers the values 0 to 127 — letters, digits, punctuation, and a set of invisible “control” characters such as newline and tab. Today we need only three ranges from it.
THE SAME THING, FOUR WAYS
A
the character
65
its ASCII code
41h
in hexadecimal
01000001
as the machine stores it
COAL · LECTURE 01
31
Notes: Keep this short — five minutes at most. Do not demonstrate any conversion; that comes much later.

## Slide 32
13 · INTRODUCTION TO ASCII
The three ranges to remember
0
32
64
96
127
THE WHOLE OF STANDARD ASCII · 0 TO 127
DIGITS
0 → 9
48 → 57
ten codes
UPPERCASE LETTERS
A → Z
65 → 90
twenty-six codes
LOWERCASE LETTERS
a → z
97 → 122
twenty-six codes
Characters are stored as numbers — and digits, uppercase letters and lowercase letters each sit in their own separate range.
ASCII also contains symbols and invisible control characters. We are not looking at those, and we are not converting anything today.
COAL · LECTURE 01
32
Notes: Three ranges, three numbers each. That is the entire ASCII requirement for today. Resist every temptation to show a conversion.

## Slide 33
14 · INTRODUCTION TO EMU8086
EMU8086 — where all of this will happen
WHAT IT IS
A program that pretends to be an 8086 computer. An emulator — bundled together with a text editor and an assembler, all in one window.
WHY WE USE IT
There is no 8086 chip on your desk, and a modern machine will not happily run 16-bit programs. The emulator gives you a complete, safe 8086 that you can stop, inspect and restart at will.
THE REAL ADVANTAGE
You can watch the registers and memory change, one instruction at a time. Nothing teaches the fetch–decode–execute loop faster than seeing it happen.
You will install it in the first lab. It is small and it runs on any machine.
1
Editor
Where you type your source code, like any other text editor.
2
Assemble / compile
Turns your source into machine code — and tells you where your mistakes are.
3
Emulate / run
Starts the virtual 8086 and runs your program from the beginning.
4
Single step
Executes exactly one instruction, then stops so you can look around.
5
Registers window
Shows the live contents of AX, BX, CX, DX and all the rest, updating as you step.
COAL · LECTURE 01
33
Notes: If you have EMU8086 open on the lecture machine, switch to it now for two minutes rather than talking over the slide.

## Slide 34
14 · INTRODUCTION TO EMU8086
What EMU8086 looks like
emu8086 — my_first_program.asm
compile
emulate
calculator
convertor
1
; my first program
2
3
.MODEL SMALL
4
.STACK 100H
5
.CODE
6
MAIN PROC
7
MOV AX, BX
8
MAIN ENDP
9
END MAIN
emulator: my_first.com
single step
run
reload
REGISTERS
AX
0000
CS
0700
BX
0000
IP
0100
CX
0000
SS
0700
DX
0000
SP
FFFE
MEMORY
0700:0100 8B C3
0700:0102 90 90
1
2
3
4
5
1
Editor
type your code
2
Compile
build it
3
Emulate
run it
4
Single step
one instruction
5
Registers
watch them change
COAL · LECTURE 01
34
Notes: A mock-up, not a screenshot — the real window is arranged slightly differently depending on version. Show the real thing live if you can.

## Slide 35
15 · READING ASSEMBLY CODE
Practice: name the parts, not the meaning
For each line, answer only this: what are the pieces called?
MOV AX, BX
MNEMONIC MOV
DESTINATION AX
SOURCE BX
MOV AL, 65
MNEMONIC MOV
DESTINATION AL — an 8-bit register
SOURCE 65 — a plain number
again: MOV CX, DX ; keep a copy
LABEL again:
MNEMONIC MOV
OPERANDS CX then DX
COMMENT after the semicolon
Notice that you still have no idea what MOV actually does. That is deliberate — and it has not stopped you reading the code.
COAL · LECTURE 01
35
Notes: Do this as a call-and-response with the room. Ask 'what is MOV called?' — answer: the mnemonic. Not 'what does it do'.

## Slide 36
16 · THE BOUNDARIES OF LECTURE ONE
What we are not doing today
So that nobody walks out worrying they missed something. None of this has happened yet — on purpose.
×
Arithmetic operations
×
Logical operations
×
What MOV actually does
×
Loops
×
Jumps
×
Conditional statements
×
Memory addressing
×
The stack
×
Procedures
×
Interrupts
×
Complete assembly programs
TODAY =
understand the machine
+
understand the language
+
get comfortable with EMU8086
Actual assembly operations begin in the next lecture. You are exactly where you should be.
COAL · LECTURE 01
36
Notes: This slide defuses the anxious student who expected to write code on day one. Say plainly: none of this is missing, it is scheduled.

## Slide 37
17 · RECAP
What you now understand
What COAL is — and why it is two subjects at once
What computer organization means
What assembly language is, and where it sits
High-level vs assembly vs machine language
The main parts of a computer, and how they connect
What is inside a CPU: control unit, ALU, registers
The fetch → decode → execute cycle
What 8-, 16-, 32- and 64-bit mean at a basic level
What x86 and x64 / x86-64 refer to
What the 8086 is, and why this course studies it
The 8086 register set — and the AH / AL split
The anatomy of an assembly statement
Syntax: case, indentation, commas, comments, labels
The shape of a complete assembly program
The three ASCII ranges: 48–57, 65–90, 97–122
What EMU8086 is, and what its main buttons do
If you can explain each of these to the person sitting next to you, lecture one has done its job.
COAL · LECTURE 01
37
Notes: Read them out and ask for a show of hands on any that feel shaky. Whatever gets the most hands is your five-minute recap at the start of lecture 2.

## Slide 38
NEXT TIME
Next lecture:
instructions that actually do something
WHAT IS COMING
What MOV really does — at last.
Moving values between registers, memory and plain numbers.
Your first complete program, assembled and run.
Watching the registers window change as each instruction executes.
BEFORE THEN
1
Install EMU8086 — we do it together in the first lab.
2
Learn the fourteen register names. Just the names.
3
Know the three ASCII ranges: 48–57, 65–90, 97–122.
4
Re-read the syntax rules. They will save you hours later.
MOV AX, BX ← you will know exactly what this means
Questions?
COAL · LECTURE 01
38
Notes: Leave real time for questions. First-lecture questions are usually the most revealing ones you will get all semester.